Traditional solid fuel burner
Applications:
- Stove
- Water heater
- Steam boiler (Rankine cycle engine / turbine)
- Ericsson cycle engine / turbine
- Stirling engine
Output:
Heat +
plant food
(CO2 , H2 O)
Secondary air
Primary air
Because of updraft gasification (happening inside), very easy to operate on a wide variety of fuels (size, moisture content)

---
Updraft / Downdraft gasification
Downdraft
- Sensitive to fuel: dry fuel, small pieces needed. (Fengyu gasifiers: 15% moisture, 10mm)
- Output gas with low tar content (if operated correctly). Except FEMA „tarmaker”
- practical for internal combustion engines (Imbert gasifier, WWII)
Updraft
- wide variety of fuels (upto 100..150mm diameter, 45% moisture content)
- Output gas has very high tar content
- not practical for internal combustion engine

---
Combined (updraft + downdraft) gasifier
Applications:
Otto cycle
Plus any of:
- Water heater
- Steam boiler (Rankine cycle engine / turbine)
- Ericsson cycle engine / turbine
- Stirling engine
Output:
Heat +
Engine fuel gas
(CO , H2)
Because of updraft gasification (happening inside), easy to operate on a wide variety of fuels (size, moisture content). Incoming air mixes with tarry „updraft” gasification gases (brown arrow), burns some of them and cracks a lot more. Reduction in bottom auger.

---
Combined (updraft + downdraft) gasifier
- Wide, closed-top hopper (~monorator)
- Bottom auger (also slices charcoal)
- Slippery „funnel” hearth
- Properly placed and designed air nozzles
Because of updraft gasification (happening inside), easy to operate on a wide variety of fuels (size, moisture content). Incoming air mixes with tarry „updraft” gasification gases (brown arrow), burns some of them and cracks a lot more. Reduction in the bottom auger.

---
Otto cycle gas engines
- Smaller heat exchanger (than Ericsson cycle or Stirling engines)
- => much cheaper than Ericsson cycle or Stirling engines (per kW).
- Readily available (engines used in cars, trucks need minor modifications)
- Appr 5kW / liter (shaft power / displacement) at 1500 RPM

---
CHP (Combined Heat and Power)
- Otto engine based plants can be made efficient in small as well (large is not a problem either), near the consumer. Power+heat > 60-90%
- The bloated rankine cycle steam turbine powerplants need to be big to be efficient (to realize very high steam volume expansion). Typically 11-35% of the input energy reaches the consumer. The rest just heats the athmosphere (cooling tower) or lost during transmission (transformers, long lines)
- Ericsson (or Brayton) cycle gas turbines are somewhere between (when minimum practical size, cost or efficiency is concerned)
- Fuel cells are promising, but (AFAIK) not yet (2010) practical for syngas or producer gas (expensive, and very sensitive to gas contamination)

---
Summary
- The (updraft + downdraft) „combined gasifier” is the fruit of a research project after appr 15 built + tested gasifiers: Imbert (including GEK) FEMA and others.
- All other designs were very sensitive to fuel size and moisture content.
- The turn-down ratio (max / min power for practical operation) is traditionally 3-10
- The turn-down ratio of the combined cycle exceeds this significantly, >15
- The 2-stage gasifier (with proper ejectors) might be even better in bigger plants (perhaps above 1MWe), although this is yet unclear and requires further research. With some chance a properly designed „combined gasifier” can win in all sizes.

---
References
Marcell Gal, Hungary, Europe
http://www.vems.hu/wiki/index.php?page=MembersPage%2FMarcellGal%2FGasProducer